The command below will help aid in the creation of forwarding rules
and is taken from https://cloud.google.com/compute/docs/load-balancing/http/global-forwarding-rules
in order to create the exsternal load balancer
and follows the archture described in https://cloud.google.com/compute/docs/load-balancing/http/
as the top component in the creation of the HTTPS load balancer
gcloud compute forwarding-rules create testforwardingrule --address 35.184.132.197 --ip-protocol TCP --ports=443-443 --target-https-proxy test-target-proxy
the next part if the creation of the Target proxy
which is described in
https://cloud.google.com/compute/docs/load-balancing/http/target-proxies
to create it we can do
gcloud compute target-https-proxies create test-target-proxy1 --url-map test --ssl-certificates test
the next component in the load balancing stack is the URL-map
as described in https://cloud.google.com/compute/docs/load-balancing/http/url-map
The URL map allows for the direction of traffic based on the inocming URL
 As there is no host rule then all then this means that all hosts will use the same path mtacher, (the path matcher is essentially a folder on the backend server so if you had a domain such as www.vinsonjewellers.com/videos the patch matcher if set to /video would direct traffic to the /video folder in the instance defined by the backend service)
As we do not have any path matchers set as it is not needed for this task the deafult path matcher is used which is /*. This means that every match is sent to the deafult service which is defined as the backend
The URL map can be created through the following command
gcloud compute url-maps create test --default-service my-backend

gcloud compute url-maps list
NAME DEFAULT_SERVICE
test backendServices/my-backend

deafult firewall rules
dc@dc-HP-Pavilion-dv7-Notebook-PC:~/Desktop/CICD/GCLOUD$ gcloud compute firewall-rules list
NAME NETWORK DIRECTION PRIORITY ALLOW DENY
default-allow-http default INGRESS 1000 tcp:80
default-allow-https default INGRESS 1000 tcp:443
default-allow-icmp default INGRESS 65534 icmp
default-allow-internal default INGRESS 65534 tcp:0-65535,udp:0-65535,icmp
default-allow-rdp default INGRESS 65534 tcp:3389
default-allow-ssh default INGRESS 65534 tcp:22

rules look good and do not look as if they require changing more reaserch is needed for internal ports on the ingress, some rules like rdp is not needed so may need to end up deleted.
ICMP is debateable as it allows hackers to map out the network or even be exposed to the ping of death if enough traffic is sent but may be usefull in the event that something goes wrong